## Slide 1: Model Checking Auto-Driving Car Features
By: Michael Dembinski

## Slide 2: Overview
Using Spin, I modeled, validated, and verified three different features of auto-driving cars. As well as command organization.
  Collision Avoidance.
  Adaptive Cruise Control.
  Lane Assistance
  Command Distribution
Will discuss the individual models as well as the validation/verification efforts. Then will report results.
First, why is this an important project?

## Slide 3: Project Motivation
Automated cars are becoming more relevant.
  Tesla
  Google self driving car
  Semi-autonomous vehicles
They all have certain common features.
  The implementation design must be ensured to be safe.
  This project has been a case of proving the need for formal methods in the system design phase.

## Slide 4: Assumptions
I began with a series of assumptions that simplified the problem scope to make it a feasible project.
  Semi-autonomous car
    Only contains the auto driving features discussed here
    Must always return to human control
    Must always warn before stealing control
  High level system design
    No worrying about how to actually see another car
    No worrying about sensor observer design
    No worrying about feedback control design
    Solely a system design effort using formal methods

## Slide 5: Adaptive Speed Control
Modeled as a 3 process system.
  Process 1 -> Searching
    This process searches for whether there is a car ahead or not
    Will randomly set this to true or false
  Process 2 -> Monitor
    If there is a car ahead this will monitor whether the gap is growing or shrinking, and whether this car is at the targeting following distance or not.
    Runs parallel to searching
  Process 3 -> Control
    Given certain monitor conditions this process will either accelerate or decelerate in response to the current state.
    Guards dependent on monitor, runs parallel to other two processes.

## Slide 6: Specifications
Liveness
  Must always eventually correct to not being too close.
  Must always eventually correct to not being too far.
Safety
  If too close must either decelerate or have car ahead be false.
    This is tricky, must account for situations where car leaves lane while too close leading to no car ahead and no requirement for follow distance.

## Slide 7: Validation
Iterative simulation and code review
  Ran the iterative simulation to confirm proper behavior
  Also created validation specifications for this effort as well
    Example: []!accelerate && decelerate
Global Model
  All variables in model are bools
  Created a global model to test all specifications against
    Both spec and !spec must be false somewhere within the model
    If spec is always true, then spec is pointless
    If !spec is always true, then spec is unsatisfiable

## Slide 8: Lane Assist
Modeled as 3 processes as well, similar to adaptive speed control.
Instead of maintaining gap with front car, maintain pacing between lane lines.
Must be able to account for no line situation, narrowing lanes, breached lanes, flakey line reading, and warning driver.

## Slide 9: Lane Assist
Process 1 -> Reading
  Determines if the lines are being seen or not.
Process 2 -> Monitor
  This process monitors the distance to the left line and the right line and whether they are increasing or decreasing.
  Also monitors for the case of a breach of the lane line.
Process 3 -> Control
  This process runs dependent on the Monitor
  Warns the driver if approaching lane breach.
  If breach happens, warns driver and takes mitigative action.

## Slide 10: Specifications
Liveness
  Must always return control to driver.
  Must always end up out of a breach situation.
Safety
  Must never cause a lane breach with mitigative actions.

## Slide 11: Validation
Iterative simulation and code review
  Ran the iterative simulation to confirm proper behavior
  Also created validation specifications for this effort as well
    Example breach must always be after a warning/closing situation
Global Model
  All variables in model are bools
  Created a global model to test all specifications against
    Both spec and !spec must be false somewhere within the model
    If spec is always true, then spec is pointless
    If !spec is always true, then spec is unsatisfiable

## Slide 12: Collision Avoidance
Three different processes take place.
  Collision Prediction.
  Risk Assessment.
  Avoidance Maneuver.
Collision Prediction
  This process will determine whether or not a collision is imminent.
  It will predict a collision from either the front, back, left, or right.
Risk Assessment
  Determines the danger of taking a maneuver to the front, back, left, or right.
Avoidance Maneuver.
  Takes the lowest risk maneuver in order to avoid a collision if possible.

## Slide 13: Collision Avoidance
Assumption that mitigative actions take place very quickly.
With this assumption these process do not run concurrently
  If monitor spots a situation, then a risk assessment is conducted.
  Dependent on that assessment then the appropriate action is taken.
Must make sure model allows for the possibility of a collision.

## Slide 14: Specifications
Safety
  Must always take the lowest risk situation
  Favor right swerve and braking in risk ties
Liveness
  Must always return control back to the human or end up crashed

## Slide 15: Validation
Iterative simulation and code review
  Ran the iterative simulation to confirm proper behavior
  Also created validation specifications for this effort as well
    Example: a collision is possible, or nothing is capable of happening.
Global Model
  All variables in model are bools
  Created a global model to test all specifications against
    Both spec and !spec must be false somewhere within the model
    If spec is always true, then spec is pointless
    If !spec is always true, then spec is unsatisfiable

## Slide 16: High Level Decision Making
How do you determine what to call when?
This was simplest model given my assumptions
  These are the only three automatic processes
  Only one necessitates emergency maneuvers
  Speed control is assumed to be turned on
    This is a constant process
Two processes
  One for monitoring control requests
  One for dishing out authority

## Slide 17: High Level
The distribution process runs a number of if guards
  One for each truth statement
  Assuming that speed control is a near constant task this leaves only 4 situations.
  Depending on the truth statement the steering and speed controls are dished out appropriately.
    Collision avoidance is always given priority and then the other two receive equal priority given that they control two different things.
  All features are allowed to push a warning at any time.

## Slide 18: Specifications
Liveness
  Must always result in human control again
Safety
  Never give two items control of the same item at the same time.

## Slide 19: Validation
Iterative simulation and code review
  Ran the iterative simulation to confirm proper behavior
  Also created validation specifications for this effort as well
    Example: []!accelerate && decelerate
Global Model
  All variables in model are bools
  Created a global model to test all specifications against
    Both spec and !spec must be false somewhere within the model
    If spec is always true, then spec is pointless
    If !spec is always true, then spec is unsatisfiable

## Slide 20: Results
Eventually after iterating on the design of the models and the specifications, I ended with models that successfully ran with no errors against the appropriate specs.
This was mostly a design/modelling project
The models themselves are the result

## Slide 21: Further Work
This could easily lead in to developing models for more features to define a fully automated system.
Could also lead into lower level models
  Design the risk assessment model
  Design the lane reading model
  Design the car monitor model